## Slide 1: Sensors: creating and transmitting data
A short guide about sensors and how to obtain data

## Slide 2: IoT - The story
1969
Internet
Igloo White
1968
Internet of Things
Sensor Networks
1999
1970
1980
1990
2000
2010
1982
Connected coke
vending machine
Google cars
2010
Notes: Give example on agriculture and insurance
1982: Four graduate students at the Carnegie Mellon University's School of Computer Science installed micro switches in the soda vending machine to be able to check from their desks whether the machine was stocked with drinks. This was the first Internet-connected appliance in the world.

## Slide 3
#smart cities
(bottles)
#smart cars
What allowed us to get this far?
Moore’s Law
+ miniaturization
- interaction
Sensors & ML
+ insulation
- ??
Changing the world, one thing at a time
Notes: Smart locks, smart cement, DHL tracking, smart lights.
I put the ?? to give a hint for next slide. What are the cons of enabling autonomous operation of many devices? “Well, even more will pop up, and they will consume: energy, bandwidth, generate data, security issues”
Baby monitor combined with smart thermostat.
All of these applications a simple one-to-one connections. http://www.tvilight.com/wp-content/uploads/2015/11/Sensor-Based-Wireless-Lighting-Control-Logo-80x80.png
Smart home, amazon echo, nest thermostat.
Wearables fitbit checking quality of sleep
Smart lighting for citites.

## Slide 4: Overview
Four questions:
What are sensors?
Who wants sensors and why?
Where do we put sensors?
How can we obtain the sensor data?
  Traditional communication systems
  Backscattering

## Slide 5: What?
Infrared transmitter
Infrared receiver
empty
Example: people counter
A passer-by cuts off the signal shortly
Notes: An example of a sensor that counts people

## Slide 6: What?
Anything that can measure something
Typically electronics
Field | Sensor device
Sound | Microphone
Weather | Thermometer, barometer
Localization | Compass, GPS
Mechanical | Speedometer, gyroscope
Optical | Camera, color sensor
Presence | Radar, proximity sensor
Notes: When we talk about sensors, we usually mean electronic sensors

## Slide 7: Who and why?
Universities, Institutes Doing science, data gathering
Factories Monitoring and automation
Hospitals Health checks
Tourists Photos
Anyone navigation, games, touchscreen, keyboard

## Slide 8: Who and why?
Universities, Institutes Doing science, data gathering
Factories Monitoring and automation
Hospitals Health checks
Tourists Photos
Anyone navigation, games, touchscreen, keyboard

## Slide 9: Where?
Noord/Zuidlijn project
Points of interest
Need a power connection
  Attach to lampposts
  Solar panels
Notes: Noord Zuidlijn project is an example here at AMS. Put the sensors in the city to monitor passenger flows
Solar panels is for better deployment

## Slide 10: Transfer sensor data How?
Transmit the collected data
WiFi
Any other method
LoRa
3G/4G
Notes: Rhino experiment, LoRa example

## Slide 11: Wireless communication
Three building blocks:
  Transmitter
  Sensor
  Decoder
Change the environment (speech)
Sensor
(ears)
Decode the message (listen)
Notes: You might think that speech is a soft/faint example, but speech is a pretty good example of wireless communication.
A change is made in the environment. Sound waves that form a signal.
A sensor is required to pick up the waves.
In the end, if somebody listens to the spoken language, one can understand the conveyed message.

## Slide 12: Wireless communication
Three building blocks:
  Transmitter
  Sensor
  Decoder
Transmit radio waves
Receiving antenna
Decode the message (protocol)
Notes: WiFi or other networks work the same. The only difference is the protocol. In speech, we pick a language such as English or Dutch.
For electronic communication we have protocols that tell a device how to send images, web pages, text messages and video’s.

## Slide 13: Energy consumption
Transmission takes the most energy
Transmit radio waves
Receiving antenna
Decode the message (protocol)
Notes: Transmission costs energy. Electricity is converted into radio waves (or sound, light etc)

## Slide 14: Backscattering
Save energy: reflect waves
Data by reflection
Receiver
Decode the message (protocol)
Notes: Transmission costs energy. Electricity is converted into radio waves (or sound, light etc)

## Slide 15: Backscattering
“Backscattering” of light
It’s not new
Now we have better sensors
DSET IoT: We improve sensor systems
Notes: First, example of mirror in armies
Sensor technology has improved and we are improving it

## Slide 16: Luxsenz platform
Reflect light
Light is everywhere
Prototype ready October 2018

## Slide 17: Future vision
Notes: To finish, what could we do by improving sensor Future vision based on enhanced use of existing sensors